## Slide 1: Virtual cluster

## Slide 2: Virtual cluster
VC is a many-to-one virtualization technology
It can form a routing system from multiple common devices connected through a switching network
While performing the same as a single logical router to all external appearances

## Slide 3: Purpose
To increase core layer device capacity and scalability, a simpler and easy-to-maintain network structure that meets core switching and interconnection network requirements is used,
Using current technologies, there are three ways to solve the capacity problems that affect core devices:
1.single device capacity expansion
2.routing interconnection
3.multiple router cluster

## Slide 4: three ways to solve the capacity problems that affect core devices:
1. Single device capacity expansion
* The first way is to increase the number of slots on the chassis of each router and enlarge the capacity of each individual interface.
2. Routing interconnection
The second way is to extend multiple routers through routing interconnection.
This requires the use of many additional high-speed interfaces, increasing the interconnection link overhead, and introduces issues with addresses, protocol neighbours, routing entries, and extending convergence time, among others.
In this way, networks become more complex and harder to maintain,
3.Multiple router
third way is to use cluster technologies across multiple routers.
This makes maintenance easy and does not increase network complexity, using more cost-effective means to meet rapid service growth, network performance, and capacity improvement requirements.

## Slide 5: two types of router cluster technology: physical clusters and virtual clusters.
Both are horizontal clusters, consisting of two or more devices composing a single logical device that appears on the network to be a single router.
, only clusters comprised of two back-to-back chassis are used as examples. n
  A physical cluster consists of two backbone routers connected to one another through a dedicated board and dedicated cables.
  Advantages: dedicated hardware ensures unblocked connection,
  dedicated hardware
  fault detection mechanism ensures high fault protection performance.
  Disadvantages: dedicated hardware is expensive and requires that the chassis be close to one another.
  A virtual cluster consists of two edge routers connected to one another through a common interface board and an inter-board trunk
  . Unlike physical clusters, this router cluster technology can be blocked and so requires users to properly plan interconnected bandwidth.
  Inter-chassis connection fault detection and switchover performance is poor in comparison to a physical cluster, being equivalent to that of a common trunk.
  However, because it lacks dedicated hardware, it is inexpensive and the chassis can be further away from each other than with a physical cluster.
Due to the preceding factors, the two router cluster technologies are applied differently. In general, physical clusters are used for backbone networks, and virtual clusters are used for DC egress and metro networks.

## Slide 6: benefits
Virtual cluster cannot only be used to expand the capacity of routers on the live network and increase their forwarding capacity.
It can also be used to replace the traditional two-node cluster protection, there by greatly simplifying network design, in turn reducing network manpower and costs.